## Slide 1: VNS Tomography Phoenix Training
XtremeGeo LLC
Fall 2025

## Slide 2: Comments
You will almost certainly create more than one model!
It’s generally recommended that the first model be somewhat coarse:
  Large horizontal node spacing, 50m or so
  Not too many vertical nodes, 30 or less
  Inversion run with large decimation, 5 or more
One key reason for a coarse initial model is to ensure that the model is deep enough

## Slide 3: Steps
Create an initial model
Define the starting velocity using the moveout trend (optional but highly recommended)
Run an inversion. It’s likely more than one will be run using different offsets, decimations, etc.
QC the solution:
  View the “Pick QC” display
  Shot/station tomo stacks (very important!!!)
  View profiles
  Map displays
  Apply the solution in a picker window, ensure flatness
Model editing, if needed
Generate statics

## Slide 4: New model
Click “VNS” then select “Create new VNS model”
Be sure to give the new model a memorable, clear name. You will soon have more than one model!
Horizontal node spacing is 150 feet, quite large – recall that this is a “test” model
Optionally, left-click and drag on the map to define grid angle.
The initial velocity field in not important since it will be defined using the moveout trend curves
The node layout method is important. The “Flat bottom” layout method generally works very well. In this example the bottom elevation is set to 4,000 feet

## Slide 5: Define initial velocity field using moveout trend
If needed, define an accurate moveout trend
In the tomography window click “Modifications” then select “Import: Generate velocity field from moveout trend picks”
You will be given the option to create a new model. There’s no need to create a new model at this point, just overwrite existing velocity field
The application will generate first break picks along the trend curves and perform a 1D Eikonal inversion at each picked location. This inversion yields an accurate velocity field at each location
The velocity to interpolated to the rest of the model
The result is a high-quality initial velocity field
Some contractors will deliver this as a final product – please don’t!

## Slide 6: Before running inversion, look at Pick QC display
Left-click on a shot
Red are user picks, blue predicted by model

## Slide 7: Inversion
Click “Analysis” then “Model update – standard approach”
Modify the name, if desired. Running the inversion will not overwrite the current model
Select the desired offset range
A decimation of “1” means no decimation!
Select decimation greater than 1 for the first pass
Ignore VTI for now. Be aware though that including VTI can have a significant impact
Leave the bottom two options unchecked – We want to understand how “good” the initial model is

## Slide 8: Inversion
Select correct pick version

## Slide 9: Inversion
The “huge survey…” option is useful for the largest surveys, especially when running on an MPI cluster
The huge survey approach tiles the survey, based on thread availability

## Slide 10: Inversion
This option is useful if, for example, there are regions of receivers without nearby shots.

## Slide 11: Inversion
This rarely used option can be used to ignore offset ranges where the picks have issues. For example, heavily shingled data

## Slide 12: Inversion
During the first inversion it may be a good idea to force the velocity to increase with depth.
Otherwise, usually allow inversions

## Slide 13: Inversion
Constraining inversions is covered in another document

## Slide 14: Inversion
The default depth weighting scheme usually converges fastest

## Slide 15: Inversion
Vertical smoothing is usually not recommended, but may be needed to help stabilize the solution
Horizontal smoothing can help avoid artifacts.
  Not much at the surface, “0” or “1’
  At the bottom, usually around “3” to “6”

## Slide 16: Inversion
These options help avoid artifacts caused by low fold or incomplete offset range coverage.
Usually only the first option is used
Will revisit this in a bit…

## Slide 17: Inversion
If running locally be sure to specify the number of threads
Selecting one of the MPI options will open another dialog

## Slide 18: Inversion
The inversion runs as a batch job

## Slide 19: Open the new model
Click “VNS”  “Reload list of models”
The click “VNS” and select the new model
The next step is to QC the model…

## Slide 20: View the model history

## Slide 21: View the velocity field at several depths
Select “Layer from 3D volume”
Then view different depths

## Slide 22: Pick QC display
Select the “Pick QC” tab
Select the pick version used to
run the inversion
Color the basemap by the
VNS residual error term
Red are user picks, blue predicted by tomo

## Slide 23: Error histogram
Note the Average Error is 7.6 Milliseconds

## Slide 24: Shot picker QC -
Open a new Shot picker display
In the flow builder add “Apply VNS tomography travel times”, found under the “Moveout options”
Experiment with the residual terms
Under the basemap “Options” tab select the VNS model, then color by the VNS error term
View several shots

## Slide 25: Profiles
Select the “Profile” tab
Left-click and drag profile lines
The “Weight” attribute shows raypath coverage. Be sure to select “Log scale”
This is a serious issue – the raypath coverage is very high along the
bottom of the profile. This means the model is not deep enough!!!
We need to create a new model…

## Slide 26: Initial model not deep enough!
Reduced horizontal node spacing to 82.5 feet
Increased vertical node count to 50
Decreased bottom elevation to 2,500 feet (from 4,000 feet)
After creating the model run an inversion
using the same options
Create a new model

## Slide 27: Open the new model and select the Profile tab
Note that the raypaths did not reach the bottom of the model – good news!
The lowest valid elevation is about 3,000 feet. The intermediate datum should not be less than that.

## Slide 28: Histogram plot of new model,
Error Reduced to 6.3 Milliseconds

## Slide 29: Create shot/station stacks as a final QC and to optionally update the shallow velocity field
Select the Shot/station stacks tab
Then click the green “+”
The new model looks better

## Slide 30: Stack options
You will likely have more than one stack, so use a descriptive name
The stack runs on the local machine as a batch job, the more threads the better
A decimation of “1” means no decimation!
Select an offset range
The Residual term is NOT applied
when creating the stacks!!

## Slide 31: Stacks
Experiment with different
grouping methods
Short wavelength variation is mostly caused by unresolved very shallow velocity field

## Slide 32: Pick the stacks
The pick times are a measurement, in milliseconds, of the
error of the shallow velocity field

## Slide 33: Create a new model
Select the update tab
Give the new model a name
Select the “Just use deviations from mean” to avoid bulk shifts.
Select a modification depth. Phoenix will compute a modification to the velocity field at each shot and station that accounts for their pick times, and blend that change into the model
Modify the Velocity Field Using the Stack Pick Times

## Slide 34: Open the new VNS model
We expect that the stacks on the new model will have fewer short wavelength artifacts
Reload the list of VNS models and open the new model
QC the new model –
  View the velocity field on the map
  Pick QC display
Create shot/station stacks
Then pick the stacks again

## Slide 35: Stack comparison on receiver line 2078
Initial stacks
After velocity update

## Slide 36: Comment
The new model might do a better job estimating the shallowest layers and produce flatter stacks
But this is no guarantee that it will produce better statics!

## Slide 37: Comparing models in profile view Select “Displays” and select “Profile comparison display”
Select the two models of interest
Choose “Elevation” profiles
Left-click and drag profiles on map

## Slide 38: Model editing using polygon
Note that the velocity field at the surface
is very large.
This error is caused by lack of low offset
traces

## Slide 39: Model editing using polygon
Select “Define polygon”
Then surround the bad zone with a polygon

## Slide 40: Model editing using polygon
Click “Modifications”  “Polygon edit – any attribute”
Be sure to create a new model!!!
Select the attribute, Velocity in this case
Choose “Edit inside polygon”
After clicking “OK” reload the list of VNS models and open the new model

## Slide 41: Statics computation
Navigate back to the VNS model window and select “Statics”  “Shortcut”
It is usually a good idea to tie the statics to the elevation statics – this ensures that the two fields have the same average value, making stack comparisons easier